## Slide 1
COMPUTER NETWORKS | ROUTING PROTOCOLS
IGRP & EIGRP
Interior Gateway Routing Protocol
& Enhanced Interior Gateway Routing Protocol
CISCO PROTOCOLS
DISTANCE VECTOR

## Slide 2
SECTION 01
What is IGRP?
IGRP = Interior Gateway Routing Protocol
Made by Cisco in 1985. It is used to share routing information between routers inside one network (called Autonomous System). It replaced the older RIP protocol.
Made By
Cisco (1985)
Type
Distance Vector
Algorithm
Bellman-Ford
Easy to Remember: IGRP is like a smart GPS for routers — it finds the BEST path using speed (bandwidth), distance (delay), traffic (load), and road quality (reliability).

## Slide 3
IGRP Key Features
Section 02
Composite Metric (5 values)
Uses Bandwidth + Delay + Load + Reliability + MTU
Not just hop count like RIP — much smarter!
Classful Protocol
Works with fixed subnet sizes only.
Does NOT support VLSM (Variable Length Subnets).
Max Hops = 255
Default is 100 hops. Maximum allowed is 255.
RIP only allows 15 hops — IGRP handles bigger networks.
Update Every 90 Seconds
Sends full routing table to neighbors every 90 sec.
Hold-down timer = 280 sec to prevent loops.
Unequal-Cost Load Balancing
Can split traffic on paths with DIFFERENT metrics.
Unique to IGRP — most protocols don't do this.
Cisco Proprietary
ONLY works on Cisco routers.
Cannot be used with other brands (Juniper, HP etc).

## Slide 4
SECTION 02b
Autonomous System (AS)
An Autonomous System is a group of routers that are managed by ONE organization and share the SAME routing protocol. Think of it as one company's private network.
🔢
AS Number Range
1 – 65535
🔗
Same AS Required
All routers must have the same AS number to exchange routes
🏢
Single Management
One organization controls all routers in the AS
⏱️
Update Timer
Routing table sent to neighbors every 90 seconds

## Slide 5
Why IGRP Was Replaced — Its Weaknesses
Section 03
✗
No VLSM / CIDR Support
Classful only — can't use subnets of different sizes. Modern networks NEED this.
✗
Slow Convergence
Takes minutes to update after a link fails. Network stays broken during this time.
✗
No IPv6 Support
Never updated for IPv6. Dead end for modern networking.
✗
Cisco Proprietary Only
Can't work with non-Cisco routers. Bad for multi-vendor networks.
✗
Periodic Updates Waste Bandwidth
Sends full table every 90 sec even when nothing changed.

## Slide 6
SECTION 04
What is EIGRP?
EIGRP = Enhanced Interior Gateway Routing Protocol
Made by Cisco in 1992. It is the UPGRADED version of IGRP. It is called a 'Hybrid' protocol because it works like Distance Vector but also uses some Link State features. Became open standard in 2013 (RFC 7868).
Year
1992 (Cisco)
Open: 2013
Type
Hybrid Protocol
(DV + Link State)
Algorithm
DUAL
(Diffusing Update)
IP Protocol
Number 88
(Not TCP/UDP)
Multicast IP
224.0.0.10
(Used for updates)
Transport
RTP – Reliable
Transport Protocol

## Slide 7
EIGRP Technical Details
Section 05
RTP — Reliable Transport Protocol
• EIGRP uses its OWN transport — NOT TCP or UDP
• RTP makes sure packets are delivered reliably
• It also supports multicast AND unicast sending
Multicast Address: 224.0.0.10
• EIGRP sends updates to address 224.0.0.10
• Only EIGRP routers listen to this address
• Saves bandwidth — not sent to all devices
IP Protocol Number 88
• EIGRP uses IP protocol 88 (not TCP=6 or UDP=17)
• This is how IP knows to pass packet to EIGRP
• Similar to OSPF which uses protocol 89
Unequal-Cost Load Balancing
• Can share traffic across paths with DIFFERENT metrics
• Use 'variance' command to set how unequal they can be
• IGRP also had this, EIGRP keeps and improves it

## Slide 8
SECTION 05b
EIGRP Maintains 3 Tables
Every EIGRP router keeps 3 separate tables in its memory. You must know these for exam!
1. Neighbor Table
Answers:
WHO is connected to me?
Stores:
IP of neighbor, interface, hold timer
Updated:
Updated by HELLO packets every 5 sec (LAN) / 60 sec (WAN)
Tip:
If Hello stops → neighbor removed → routes deleted
2. Topology Table
Answers:
ALL routes I know about
Stores:
Successor route + Feasible Successor (backup route)
Updated:
Updated by UPDATE packets from neighbors
Tip:
Contains EVERY possible path, not just the best one
3. Routing Table
Answers:
BEST routes for forwarding packets
Stores:
Only the Successor (best) routes
Updated:
DUAL picks best from Topology Table
Tip:
This is what the router actually USES to forward traffic

## Slide 9
DUAL Algorithm — How EIGRP Finds Best Path
Section 06
DUAL = Diffusing Update Algorithm. It is the brain of EIGRP. It picks the BEST (Successor) route and keeps a BACKUP (Feasible Successor) route ready. If primary fails, backup is used INSTANTLY — no waiting!
MY ROUTER
DESTINATION
PATH A
Successor
Metric: 1000
BEST ROUTE
(Used for forwarding)
PATH B
Feasible Successor
Metric: 1500
BACKUP ROUTE
(Ready if A fails)
Uses PATH A normally
Switches to B if A fails

## Slide 10
IGRP vs EIGRP — Quick Comparison Table
Section 07
IGRP
EIGRP
Year
1985
1992 (Open: 2013)
Type
Distance Vector
Hybrid (DV + Link State)
Algorithm
Bellman-Ford
DUAL Algorithm
Subnet Support
Classful only
Classless (VLSM ok)
Convergence
Slow
Very Fast
Max Hops
255 (default 100)
224 (default 100)
Updates
Every 90 sec (full table)
Only when change happens
Load Balancing
Unequal-cost
Unequal-cost (improved)
IPv6 Support
No
Yes (EIGRPv6)
Transport
IP Protocol 9
IP Protocol 88 + RTP

## Slide 11
Quick Revision — All Key Points
!
1
IGRP — Made by Cisco 1985. Distance Vector. Uses Bellman-Ford. Classful. Max 255 hops. Updates every 90 sec.
2
IGRP Metric = Bandwidth + Delay + Load + Reliability + MTU (5 K-values). Much smarter than RIP's hop count.
3
IGRP Weakness = No VLSM, slow convergence, Cisco-only, no IPv6. That's why EIGRP replaced it.
4
EIGRP — Made by Cisco 1992. Hybrid (DV + LS). Uses DUAL algorithm. IP protocol 88. Multicast 224.0.0.10.
5
EIGRP uses RTP (Reliable Transport Protocol) for its own reliable delivery — NOT TCP or UDP.
6
EIGRP 3 Tables: Neighbor Table (who) + Topology Table (all routes) + Routing Table (best routes).
7
DUAL keeps a Successor (best path) and Feasible Successor (backup). If primary fails → backup used INSTANTLY.
8